March 2014

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5617 BA Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Robert Bosch (SEA) Pte Ltd, Security Systems 11 Bishan Street 21 Singapore 573943 Phone: +65 6571 2808 Fax: +65 6571 2699 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 29

VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

BOSCH NDN-832 FLEXIDOME HD 1080p DAY/NIGHT IP CAMERA

- – GENERAL

  - SUMMARY

    - Section Includes

      - Video Surveillance Remote Devices.

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 19 – Digital Video Recorders and Analog Recording Devices].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - European Norm

      - CE Declaration of Conformity

      - EN50121-4 (CE) – Railway applications – Electromagnetic compatibility. Emission and immunity of the signaling and telecommunications apparatus.

      - EN50130-4 (CE) (PoE, +12 VDC, 24 VAC) Alarm Systems, Part 4 – Electromagnetic Compatibility – Product Family Standard: Immunity Requirements for Components of Fire, Intruder and Social Alarm Systems

      - EN55022 class B (CE) – Information Technology Equipment – Radio Disturbance Characteristics – Limits and Methods of Measurement for Emission

    - Federal Communications Commission (FCC) (www.fcc.gov)

      - FCC CFR 47 part 15 class B – Telecommunications – Radio Frequency Devices – Digital Device Emission.

    - HD Standards

      - Complies with the SMPTE 274M-2008 standard

      - Complies with the 296M-2001 standard

    - International Electrotechnical Commission (IEC)

      - Camera with 500 g (1.1 lb) lens according to IEC 60068-2-6 (5 m/s2, operational)

    - International Organization for Standardization (ISO)

      - 9001 – Quality System.

    - Safety

      - EN60950-1 (CE) - Information technology equipment. Safety. General requirements

      - UL60950-1 Second Edition - Information technology equipment. Safety. General requirements

      - CAN/CSA 22.2 No 609501-1 - Information technology equipment. Safety. General requirements

    - Underwriters Laboratories, Inc. (UL) (www.ul.com)

      - UL certified

    - Vibration

      - Camera with lens as per IEC60068-2-6 (5 m/s2, operational)

  - DEFINITIONS

    - Day/Night (infrared sensitive): A camera that has normal color operation in situations where there is sufficient illumination (day conditions), but where the sensitivity can be increased when there is little light available (night conditions). This is achieved by removing the infrared cut filter required for good color rendition. The sensitivity can be further enhanced by integrating a number of fields to improve the signal-to-noise ratio of the camera (this may introduce motion blur).

    - Privacy Masking: The ability to mask out a specific area to prevent it from being viewed in order to comply with privacy laws and particular site requirements.

    - SensUp (sensitivity up): Increases camera sensitivity by increasing the integration time on the CMOS. This is accomplished by integrating the signal from a number of consecutive video fields to reduce signal noise.

    - Smart BLC (Back Light Compensation): Smart back-light compensation allows the camera to automatically compensate for bright areas of a high contrast scene without having to define a window or area.

  - SYSTEM DESCRIPTION

    - Video Surveillance Remote Devices

      - NDN-832 FlexiDome HD 1080p Day/Night IP Camera

    - Performance Requirements

      - 1/2.7-inch day/night CMOS with progressive scan.

      - High resolution 1080p, HD format.

      - Local storage with microSD card.

      - Quad-streaming IP video.

      - Motorized automatic back focus.

      - High-impact, vandal-resistant enclosure.

      - ONVIF conformant.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00].

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

      - Manufacturer’s quality system: Registered to ISO 9001 Quality Standard.

    - Video Surveillance System

      - Listed by [UL] [EN] [FCC] specifically for the required loads.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [5] years experience installing Video IP Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5617 BA Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Bosch Security Systems Pte Ltd

Robert Bosch (SEA) Pte Ltd, Security Systems

11 Bishan Street 21

Singapore 573943

Phone: +65 6571 2808

Fax: +65 6571 2699

apr.securitysystems@bosch.com

www.boschsecurity.com]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

**********Specifier’s note: Select Camera System Series based on project requirement.

  - BOSCH NBN-832 DINION HD 1080p DAY/NIGHT IP CAMERA [NDN-832-V02-P] 
[NDN-832-V02-IP] [NDN-832-V03-P] [NDN-832-V03-IP] [NDN-832-V09-P] 
[NDN-832-V09-IP]

    - General Characteristics:

      - The day/night HD camera shall deliver true 1080p HD resolution in 16:9 format.

      - The day/night HD camera shall be capable of operating as an indoor/outdoor camera with an operating temperature range of

        - [Non-IVA: -50°C to 55°C (-58°F to 131°F).]

        - [IVA: -50°C to 50°C (-58°F to 122°F).]

      - The day/night HD camera shall be rated to IP67 (NEMA 4X) standard against water and dust ingress.

      - The day/night HD camera shall be rated to IK10 vandal resistance.

      - The day/night HD camera shall provide direct network connection using H.264 and JPEG compression and bandwidth throttling to efficiently manage bandwidth and storage requirements while delivering outstanding image quality.

      - The day/night HD camera shall work with Power over Ethernet IEEE 802.3af (802.3at Type 1) for indoor applications with a compliant power supply source.

      - The day/night HD camera shall support AutoMDIX.

      - The day/night HD camera shall conform to the ONVIF standard.

      - A user shall be able to view video on a PC using a Web browser, with the Bosch Video Management System, Bosch Video Client or Bosch Recording Station.

      - The day/night HD camera shall be capable of integration with third-party video management software, specifically Milestone and Genetec.

      - The day/night HD camera shall provide MOTION+ video motion detection analysis system that provides basic video content analysis.

      - The day/night HD camera shall offer Intelligent Video Analysis (IVA) in a hardware-enhanced version.

      - The day/night HD camera shall provide four (4) independent, fully programmable privacy mask areas.

      - The day/night HD camera shall provide an on-screen display to simplify the camera/lens back focus and network configuration settings.

    - Imaging

      - The day/night HD camera shall utilize a 1/2.7-inch day/night CMOS image sensor.

      - [The day/night HD camera shall utilize a 1.8 to 3 mm optically corrected ultra wide angle lens.]

      - [The day/night HD camera shall utilize a 3.8 to 13 mm optically corrected wide angle lens.]

      - [The day/night HD camera shall utilize a 9 to 40 mm optically corrected telephoto lens.]

      - The day/night HD camera shall produce a resolution of 1920 x 1080 pixels (HD 1080p) at 30 ips with a 16:9 aspect ratio.

      - The day/night HD camera shall provide a frame integration mode (Bosch SensUp feature) that can increase the integration time up to 10 times on the CCD.

      - The day/night HD camera shall produce a color image with a minimum scene illumination of 0.22 lux (0.022 fc) and a monochrome image, when in the night mode, with a minimum illumination of 0.05 lux (0.005 fc) at 30 IRE.

      - The day/night HD camera shall provide enhanced night viewing through the increase of IR sensitivity by automatically switching a motorized IR filter from color to monochrome operation in low-light or IR illuminated applications. Allow the IR filter to be switched manually via the alarm input, preprogrammed in a camera mode or profile.

      - The day/night HD camera shall utilize pixel-by-pixel analysis to automatically compensate for bright areas of a high contrast scene (Back light) without having to define a window or area.

      - The day/night HD camera shall offer 76 dB digital wide dynamic range (92 dB with iAE).

    - Housing

      - The day/night HD camera shall come fully assembled with an integral varifocal lens inside a cast-aluminum housing with a polycarbonate window and a hardened inner liner.

      - The day/night HD camera shall be able to withstand the equivalent of 55 kg (120 lbs) of force.

      - The day/night HD camera shall be protected against water and dust to IP67 (NEMA 4X) standard.

    - HD Characteristics

      - The day/night HD camera shall generate full HD 1080p resolution and 720p resolution using H.264 compression.

      - The camera shall generate multiple simultaneous video streams:

        - Two Independently Configurable H.264 Streams:

          - Stream 1:

            - H.264 Main Profile (MP) 1080p 25/30,

            - H.264 Main Profile (MP) 720p 25/30

or

H.264 MP Standard Definition (SD)

          - Stream 2:

            - Copy of stream 1 (when 1080p),

            - H.264 Main Profile (MP) 720p 25/30 (when stream 1 is 720p)

or

H.264 MP Standard Definition (SD)

        - Two Additional Streams

          - M-JPEG stream

          - High Definition (HD) I‑frame only stream

      - The day/night HD camera shall offer G.711 audio standard at an 8 kHz sampling rate AAC.

    - Installation Requirements

      - The day/night HD camera shall be capable of operating in an outdoor environment within the following temperature ranges:

        - [Non-IVA: -50°C to 55°C (-58°F to 131°F).]

        - [IVA: -50°C to 50°C (-58°F to 122°F).]

      - The day/night HD camera shall contain a pan/tilt/zoom mechanism that allows selecting the exact field of view.

      - The day/night HD camera shall offer surface, wall, and suspended ceiling mounting options.

      - The day/night HD camera shall provide power, video, and control via an Ethernet connection.

      - The day/night IP camera shall be capable of simultaneous connection to both PoE and 12 VDC / 24 VAC power supplies.

      - The day/night HD camera shall provide a multi-language on-screen display.

    - Storage Management

      - The day/night HD camera shall support iSCSI devices to allow video stream to be recorded directly to an iSCSI RAID array.

      - The day/night IP camera shall support iSCSI storage targets to enable the camera to function as a conventional DVR.

      - The day/night IP camera shall have a microSD card slot that uses standard, off-the-shelf microSD SDHC or SDXC cards for local storage (up to 2 TB).

      - The local storage feature shall be capable of storage for Automatic Network Replenishment (ANR).

    - Alarm Handling Features:

      - The day/night HD camera shall provide an alarm input that may be triggered by either a normally opened or normally closed contact.

      - The day/night HD camera shall provide the capability on alarm to display up to a 17 character, programmable alarm message.

      - The day/night HD camera shall provide a relay output that may be selected for normally opened or normally closed operation. The relay can be activated from an external alarm input to the camera, manual activation from the browser, upon video motion detection, or video loss.

    - IP Connectivity

      - The day/night HD camera shall allow full camera control and configuration capabilities over the network.

      - The day/night HD camera shall offer Power over Ethernet (IEEE 802.3at Class 3) for indoor applications.

      - The day/night HD camera shall deliver 1080p HD video, at rates up to 25/30 images per second, via TCP/IP over Shielded Cat5/Cat6 cable.

      - The day/night HD camera shall conform to the ONVIF standard.

      - [The day/night HD camera shall offer Embedded Intelligent Video Analytics (IVA) as a hardware-enhanced version.]

    - Embedded Video Content Analysis

      - The day/night HD camera shall be VCA enabled.

      - The day/night HD camera shall offer MOTION+ video motion analysis that uses an algorithm based on pixel change.

      - The day/night HD camera MOTION+ feature shall include object size filtering and tamper-detection capabilities.

    - [Intelligent Video Analysis

      - The day/night HD camera shall be capable of processing and analyzing video within the camera itself, with no extra hardware required.

      - The day/night HD camera shall be capable of detecting and sending alarms for abnormal events.

      - The day/night HD camera shall allow users to set up to 10 separate profiles and switch profiles based on a day/night or holiday schedules.]

    - Access Security

      - The day/night HD camera shall offer three levels of password protection.

      - The day/night HD camera shall support 802.1x authentication using a RADIUS (Remote Authentication Dial In User Service) server.

      - The day/night HD camera shall store a SSL certificate for use with HTTPS.

      - [The day/night HD camera shall be capable of being independently AES encrypted with 128-bit keys.]

    - Specifications

      - Electrical:

        - Power Supply:

          - 12 VDC ± 10%

          - 24 VAC ± 10%, 50/60 Hz

          - PoE 48 VDC nominal

        - Current Consumption:

          - 12 VDC: 0.8 A

          - 12 VDC with IVA: 1 A

          - 24 VAC: 0.7 A

          - 24 VAC with IVA: 0.8 A

          - PoE (48 VDC): 0.25 A

          - PoE (48 VDC) with IVA: 0.3 A

        - Power Consumption with Heater On:

          - 12 VDC: 9.6 W

          - 12 VDC with IVA: 11 W

          - 24 VAC: 13.4 W

          - 24 VAC with IVA: 15.8 W

          - PoE (48 VDC): 12.2 W

          - PoE (48 VDC) with IVA: 13.4 W

        - Power Consumption with Heater Off:

          - 12 VDC: 4.8 W

          - 12 VDC with IVA: 6 W

          - 24 VAC: 8.4 W

          - 24 VAC with IVA: 10.8 W

          - PoE (48 VDC): 7.2 W

          - PoE (48 VDC) with IVA: 8.4 W

    - Sensor

      - Type: 1/2.7-inch CMOS

      - Active Pixels: 1920 x 1080

    - Video

      - Video Compression: H.264 (ISO/IEC 14496‑10), M-JPEG, JPEG

      - Streaming: Four (4) individually configurable streams in H.264 and M-JPEG, configurable frame rate and bandwidth

        - Two Independently Configurable H.264 Streams:

          - Stream 1:

            - H.264 Main Profile (MP) 1080p 25/30,

            - H.264 Main Profile (MP) 720p 25/30

or

H.264 MP Standard Definition (SD)

          - Stream 2:

            - Copy of stream 1 (when 1080p),

            - H.264 Main Profile (MP) 720p 25/30 (when stream 1 is 720p)

or

H.264 MP Standard Definition (SD)

        - Two Additional Streams

          - M-JPEG stream

          - High Definition (HD) I‑frame only stream.

      - HD Resolution (H x V):

        - 1080p: 1920 x 1080

        - 720p: 1280 x 720

      - 480p Resolution (H x V)

        - Encoding: 704 x 480

        - Displayed: 854 x 480

      - 240p Resolution (H x V)

        - Encoding: 352 x 240

        - Displayed: 432 x 240

      - Overall IP Delay:

        - Minimum: 120 ms

        - Maximum: 240 ms

      - GOP Structure: IP, IBP, IBBP,

      - Sensitivity ( 3200K, Scene Reflectivity 89%, F1.2)

        - Minimum Illumination (30 IRE):

          - Color: 0.22 lx (0.022 fc)

          - Monochrome: 0.05 lx (0.005 fc)

      - Day/Night: Color, Mono, Auto

      - White Balance:

        - ATW (2500 to 10000K)

        - ATW hold and manual

      - Shutter: Auto (1/50 [1/60] to 1/50000) automatic fixed selectable

      - Backlight Compensation: On/Off

      - Contrast Enhancement: On/Off

      - Sharpness: Level selectable

      - Privacy Masking: Four (4) independent areas, fully programmable

      - Video Motion Analysis: MOTION+ or IVA option

    - Audio

      - Standard: G.711, 8 kHz sampling rate AAC

      - Signal-to-Noise Ratio: >50 dB

      - Audio Streaming: Full duplex / Half duplex

    - Input/Output

      - Audio: 1 x mono line in, 1 x mono line out

        - Connector: 3.5 mm stereo jack

        - Signal Line In: 12 kOhm typical, 1 Vrms max.

        - Signal Line Out: 1 Vrms at 1.5 kOhm, typical

      - Alarms: 2 inputs

        - Activation Voltage: +5 VDC to +40 VDC (+3.3 VDC with DC-coupled 
22 kOhm pull-up resistor)

      - Relay: 1 output

        - Voltage: 30 VAC or +40 VDC Max 0.5 A continuous , 10 VA

      - Data Port: RS-232/422/485

    - Local Storage

      - Memory Card Slot: Supports SDHC and SDXC microSD cards up to 2 TB

      - Recording: Continuous recording, ring recording, alarm/events/schedule recording

    - Software Control

      - Unit Configuration: Via Web browser or Configuration Manager

      - Software Update: Flash ROM, remote programmable

    - Network

      - Protocols: RTP, RTSP, Telnet, UDP, TCP, IP, HTTP, HTTPS, FTP, DHCP, 
IGMP V2/V3, ICMP, ARP, SMTP, SNTP, SNMP, 802.1x, UPnP

      - Encryption: TLS 1.0, SSL, AES (optional)

      - Ethernet: STP, 10/100 Base-T, auto-sensing, half/full duplex, RJ45

      - PoE Supply: IEEE 802.3at compliant

    - Mechanical:

      - Dimensions (D x H): 208 x 151 mm (8.2 x 5.59 in.)

      - Weight: 2200 g (4.85 lb)

    - Environmental:

      - Operating Temperature Range (Non IVA): -50°C to +55°C (-58°F to 131°F)

      - Operating Temperature Range(with IVA) :-50°C to +50°C (-58°F to 122°F)

      - Storage Temperature Range: -30°C to +70°C (-22°F to 158°F)

      - Operating Humidity: 20% to 93% relative humidity

      - Storage Humidity: up to 98% relative humidity

      - Vandal Resistance: IK10

      - Ingress Resistance: IP67, NEMA 4X

  - ACCESSORIES

    - VDA-832FHD-WMT Wall mount bracket for HD FlexiDomes

    - VDA-832FHD-PMT Pendant mount bracket for HD FlexiDomes

    - S1460 Service/Monitor Cable

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMONSTRATION

    - Demonstrate at final inspection that video management system and devices function properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.